ALERT CONDITION 1

HURRICANE RED/BLACK

24 HOURS PRIOR TO

SUSTAINED WINDS IN EXCESS OF 74 MPH

- FLY TWO HURRICANE FLAGS.

- LOCK ELEVATOR TO TOP FLOOR. TURN IT OFF.

- TURN OFF ALL LIGHTS.

- PUT OFFICE MACHINES IN PLASTIC BAGS.

- LOCK BATHHOUSE DOORS AND TURN BATHOUSE AIR CONDITIONING OFF.

- TURN OFF ALL WATER MAINS.

- TURN OFF MAIN ELECTRIC BREAKER IN WAYNE’S WORLD.

- TURN OFF ELECTRICITY TO EACH DOCK AT THE MAIN DOCK BREAKERS (3).

- SECURE AND LOCK ALL OUTBUILDINGS.

- SECURE PROPANE AND SHUT OFF VALVES.

- LOCK ALL CLUB DOORS ON THE TOP AND BOTTOM FLOORS AND PUT DUCT TAPE ALONG THE BOTTOM TO SEAL OUT WATER.  DO NOT FORGET SLIDING GLASS DOORS.

- ENSURE NO ONE IS ON THE PREMISES AND LEAVE.